- Unpack and remove all shipping hardware, per the “Unpacking Instructions”.

- Set up Printer (Page 15 of User Manual).

  - Check endstop locations.  Make sure they were not misaligned in shipment.

  - Plug in USB cable.  

The square end of the USB cable should be inserted with the flat side towards the printer.

  - Turn power switch off and attach power supply.

  - Install filament guide (Page 18 of User Manual).

    - You may have to lift the nut in the channel, using the small screw driver, for the filament guide screw to engage the nut.

    - Alternatively, the filament guide may be installed without washers.

  - Insert your SD card (optional).

- Prepare printer for printing

  - Install Printrun on your computer (Page 28 of User Manual).

  - Load filament (Page 36 of User Manual).

  - IMPORTANT: Set Z home before executing any move commands (Page 39 of User Manual).

  - Print your first object - the bed calibration object “bedcalib.gco” (Page 41 of User Manual).

  - Use this object to verify the Z home is set properly and the bed is level.  Adjust if necessary.