Title: TAZ bed plate flatness analysis
Test Plan: TP-RD-0014
Document Date: 08.29.16
Test Date: 08.26.16-08.29.16
Testing Location: Aleph Mountain

PURPOSE:

The purpose of this test is to determine whether we can relax the 1.0mm flatness specification that we have on bed plates to accelerate production without a significant decrease in printer performance. Currently, fallout on the 1.0mm spec is roughly 20% of plates being delivered.

RESULTS SUMMARY:
In testing, strong positive correlations were found between the bed flatness and increasing bead height variability as well as out of round printing (dragging y-axis).

CONCLUSION:

Based on the strong relationship between the flatness of the bed and the print quality, we really want the bed to be as flat as possible in order to maintain our reputation for print quality. That being said, we still need to be able to produce printers and the 1.0mm spec has been problematic for multiple vendors to hold.

Our recommendation is to increase the allowable tolerance spec to 1.3mm for the bed plates and work with PMM and Rapid to further reduce fallout. Based off of current numbers from PMM, increasing the tolerance to 1.3mm will reduce our current fallout rate from ~20% to ~4%, while keeping our bead height variance below 0.10mm and our out of round below 0.150mm. We are confident that 1.3 is an attainable flatness spec for most manufacturers to hit.

BACKGROUND INFORMATION:

Bed plate flatness is critical in ensuring that the bed bearings are located in the same plane, so that the bed moves smoothly and accurately. A binding bed will cause truncated y-movement, causing out of round holes and poor part accuracy.

Additionally, the flatness of the bed plate is critical to the TAZ's contact based auto leveling, as it ensures that the 4 auto-leveling discs are in the same plane. If the leveling discs are tilted because of a warped plate, it will introduce error into the bed probing sequence, causing the first layer bead height to be inconsistent across the bed (see figure 1).

Figure 1: Exaggerated effects of a warped plate

Glass

In the figure above the green line is the ideal plane that we would like to measure for bed leveling, as it's parallel to the actual bed plane (blue). The orange line represents the bed plane that is actually measured if one or more of the bed leveling washers are not held parallel to the bed. This error will cause the first layer bead height to be higher on the right side than on the left.

The current flatness specification was introduced to the TAZ line by revB of the bed plate for the Ironwood line of TAZ 4 machines in response to reports from the cluster that badly warped beds were causing issues with manual leveling (re-leveling needed to be performed multiple times a week on select machines, and longer leveling screws were needed in some cases).

Mathematically, a bed plate that is out of flat by 1.3mm would have an uncertainty in the height of the contact point of the washers of 0.048mm. The AO specification for allowable differences in first layer height specify that all parts of the first layer of a print must be between 0.300 and 0.425mm thick. Given that we allow +/-0.050mm tolerance for the thickness of the bed leveling washers, allowing out of flatness of up to 1.300mm would keep us within our allowable range for first layer heights.

EQUIPMENT:

Testing was performed using several out of specification bed plates and 2 TAZ 6 machines. A pair of x.xxmm capable calipers are acceptable for measuring first layer bead height, however in this initial test an x.xxx capable micrometer was used to give more precise results.

PROCEDURE:
To start, establish a baseline using multiple known good TAZ 6 printers. Print the gcode located in shared-j/Documents/R&D/bed_flatness_testing/gcode/full_build_volume_box.gcode
 (a FBV print single layer square). Record the skirt height in the back right, back left and front right corner and find the maximum deviation between points. Also record the z-offset for later comparison.

Replace the y-axis with one built up with a bed that is a known amount out of flatness spec (for this trial we used beds that were 1.38, 1.20, 1.20, 1.18, 1.5, 1.68, and 1.44 out of flat). Rerun the test, noting the change in z-offset and the new deviation between corners. The original y-axis should be dismantled and measured for out of flatness as well in order to understand the relationship between flatness and variance in squish.

For each bed plate also run the dimensional accuracy test (shared-j/Documents/R&D/bed_flatness_testing/gcode/dimensional_accuracy_test.gcode)

TEST DATA and COMPLETE RESULTS:
Printer	z-offset	First layer bead variance	Out of flatness	Out of round (+ = x longer than y)
KT-PR0041NA-00030	-1.400	(0.117) / 0.375-0.492	1.38	0.154 / (x=20.018, y=19.864)
KT-PR0041NA-00030	-1.400	.074 / (0.371-0.445)	1.20	0.020 / (x=19.901, y=19.881)
KT-PR0041NA-00027	-1.301	(0.036) / 0.342 – 0.378	1.20	0.099 / (x=19.991, y=19.892)
KT-PR0041NA-00027	-1.326	(0.070) / (0.386-0.456)	1.18	0.104 / (x=19.956, y=19.852)
KT-PR0041NA-00030	-1.380	(.140) / (.308-.448)	1.50	0.170 / (x=20.010, y=19.840)
KT-PR0041NA-00027	-1.230	0.060 / (0.440-0.500)	0.168	0.228 / (x=19.910, y=19.682)
KT-PR0041NA-00027	-1.275	0.105 / (0.318-0.423)	1.44	0.162 / (x=19.925, y=19.763)

OTHER INFO: