1. Unpack and remove all shipping hardware, per the “Unpacking Instructions”.
2. Set up Printer (Page 15 of User Manual).
  1. Check endstop locations. Make sure they were not misaligned in shipment.
  2. Plug in USB cable.

     The square end of the USB cable should be inserted with the flat side towards the printer.
  3. Turn power switch off and attach power supply.
  4. Install filament guide (Page 18 of User Manual).
    1. You may have to lift the nut in the channel, using the small screw driver, for the filament guide screw to engage the nut.
    2. Alternatively, the filament guide may be installed without washers.
  1. Insert your SD card (optional).
2. Prepare printer for printing
  1. Install Printrun on your computer (Page 28 of User Manual).
  2. Load filament (Page 36 of User Manual).
  3. IMPORTANT: Set Z home before executing any move commands (Page 39 of User Manual).
  4. Print your first object - the bed calibration object “bedcalib.gco” (Page 41 of User Manual).
  5. Use this object to verify the Z home is set properly and the bed is level. Adjust if necessary.