1.3
Mention that Cura Lulzbot edition installs Windows drivers automatically.

1.5 Load Model File
Where to find sample models like the octopus?

1.5 Model Orientation
“The black outlined corner {of the bed}...”

1.5 Model Orientation – Rotate
Rotation defaults to 15 degree increments. Hold SHIFT to rotate by single degrees.

1.6 View Mode – Overhang
Overhang threshold angle can be set in EXPERT SETTINGS.

1.6 View Mode – Layers
Support material is viewable in this mode and will be displayed blue.

1.8
Care to add another warning about knives being sharp?

1.10 – Fill density
Densities between 0-100% will print in a cross-hatch pattern of the density specified.

p. 29
Image blowed up.

1.10 – Printing Temperature / Bed Temperature
these warnings are not needed anymore and we can recommend setting temperatures in Gcode with the new firmwares.

1.11 – Initial Layer Height
We set all our profiles with an initial layer height of .3mm to allow you to never need to readjust your initial Z-height for different materials.

1.11 Cut off..
You can also use this
option to remove the lower portion of your model, or if carefully, measured, cut your part in half for printing object as two halves.

1.11 Travel Speed
I think we have this set to 175 defualt, so may want to change normal travel speeds to 125-175mm/s