PP-MP0082_Procedure
Manufacturing Engineering
10-1-2018
Mike Rosenhagen

This is the procedure to find the critical dimensions for PP-MP0082, bed leveling washer. The dimensions we are going to look for is the thickness of the washer, the diameter of the through hole, and the diameter of the washer as a whole.

The first dimension we are going to look for is the thickness of the washer. To do this you will need a Starrett Micrometer. Once you have the micrometer make sure it is fully closed and then zero it out so you can get the best results. Take the washer in one hand and the micrometer in the other, open up the micrometer until you can slide the washer between the jaws. Slowly tighten the jaws by spinning the rough part of the knob until it firmly pinches the washer. It is vital to tighten the micrometer with the rough part of the knob because this will not over tighten and give a false reading.

The next dimension we will look for is the diameter of the through hole. To do this you will need the set of pin gauges that range from 3.8mm down to 3.3mm. I would recommend starting with a 3.5mm pin gauge and if it does not slide through the hole start going down to a lower gauge until a pin gauge can slide through snugly. If the pin gauge slides through too easily start going up in gauges till you find one that is just the right fit.

The last dimension we will find is the diameter of the whole washer. Using a set of calipers, grab the washer in one hand and slowly close the jaws of the calipers using the thumb wheel. This will make sure you do not over tighten the jaws and get a false reading.