Printer:
Model:	LulzBot TAZ Pro Desktop 3D Printer
Serial Number:	KT-PR0050-
Date Completed:
Completed by:
Configuration:
Electronics:	Archim 2.2b
Firmware:	Marlin
Nozzle:	Hardened Steel 0.5mm (2X)
Stepper driver settings:
Axis	Steps/mm	Max length	Micro step mode	Current
X	100	321mm	16 steps/step	975 mA
Y	100	303mm	16 steps/step	975 mA
Z	500	299mm	16 steps/step	975 mA
E0	420	N/A	16 steps/step	960 mA
E1	420	N/A	16 steps/step	960 mA

Offsets:
Name	Datum	Relative to	Offset	Backlash
X	E2 nozzle center	E1 nozzle center	mm	mm
Y	E2 nozzle center	E1 nozzle center	mm	mm
Z	E2 nozzle center	E1 nozzle center	mm	mm
Z offset	E1 nozzle center	Top of leveling washers	mm	N/A

Belt tensions:
Belt	Type	Length	Tension
X	Cut to length	1164	N
Y	Continuous	956	N
Z Left	Continuous	866	N
Z Right	Continuous	866	N

Subassembly QA checksheets:
- Frame QA checksheet is complete.
- Y-axis QA checksheet is complete.
- Control box QA checksheet is complete.
- Toolhead QA checksheet is complete.
- Final QA checksheet is complete.
Calibration checklist:
- The bearing conditioning (burn in) is complete.
- The X, Y and Z motion is smooth over range and speeds.
- The PEI print surface is free of bubbles and wrinkles.
- The printer passes hi-pot testing.
- Verify automatic calibration and record values.
- The wipe sequence is in center of wiper pad.
- The flat of the nozzle contacts all four bed corners.
- The z-offset is calibrated and verified.
- The bed temperature control verified.
- Test print successful.
- There is no filament error message displayed during the test print.
- Belt tensions are still within spec after burn-in and test prints.
- Print head moved to shipping position.
- The certification sticker free of air bubbles, debris, and is parallel with the edge of the case.