Subassembly:
Description:	Final Assembly
Part Number:	AS-PR0147
Date Completed:
Assembly checklist completed by:
Validated:
- There are no loose screws.
- The X and Y axis have been checked for squareness.
- Frame extrusions have been checked and are flush with no gaps.
- The USB drive can be inserted without interference.
- The filament guide tubes are not crossed over.
- The spool arms are at the intended height on the frame.
- The end stop switches are not loose.
- 10 flexible feet are installed.
- The screws that fasten the control box to the frame are torqued to spec.
- There are two caution hot stickers on the back of the x-carriage.
- The extruder mount is not loose on the x-carriage.
- The y-axis mounting brackets are flush to the extrusions and not loose.
- Filament passes through the filament guide tube without interference.
- The touchscreen functions normally.
- The belts are aligned on the idler bearings and properly tensioned.
- The case fan is spinning freely.
- The extrusion fan turns on and off as intended.
- The hot end temperature control is verified.
- The level-during-home feature works as intended and the x-axis is level.
- The cables are secure and free of interference/contact with bed motion.
- The cable connectors fully engaged and oriented correctly.
- Dual linear actuator motion is verified.
- Verify machine can be auto-homed 5x without issues.

- The zip ties are installed according to the ohai.
- The filament runout sensor has been QA validated
  Put QA sticker here

Validated by:
______________